## Slide 1: Simultaneous determination of steroid hormones and pharmaceuticals and personal care products with LC–MS/MS in feces of killer whales (Orcinus orca)
Xiangjun Liao, Andrew Ross, Neil Dangerfield Institute of Ocean Sciences, Sidney
Tanya Brown, Katerina Colbourne, Peter Ross Pacific Science Enterprise Centre, West Vancouver

## Slide 2: Outline
Introduction
Objective
Material used
Method
Results
Conclusion
Acknowledgement

## Slide 3: Introduction
Steroid hormones
  Two classes: corticosteroids & sex steroids
  Help control metabolism, inflammation, immune functions, salt and water balance, development of sexual characteristics
  Indicate stress levels
Cortisol
Estradiol

## Slide 4: Introduction
Pharmaceuticals and personal care products
  Emerging contaminants: prescription (such as antibiotics), non-prescription drugs (including ibuprofen), fragrances, detergents and others.
  Sertraline has been observed and quantified in both fish liver and fillet tissue while fluoxetine in fish liver.
  Triclosan and its transformation product methyl-triclosan were found in fish.

## Slide 5: Introduction
Whale feces
  Significant role in the ecology of the oceans
  Rich in nutrients
  Indicators of health and ecology
    Diet composition-Prey
    Contaminants
    Population-
      Psychological tension or starvation-Glucocorticoids
      Nutritional stress-Thyroid hormones
      Pregnancy- progesterone
Cortisol
Triiodothyronine

## Slide 6: Objective
Be aware of the level of Steroid hormones and Pharmaceuticals and personal care products in whale feces
Develop a simultaneous determination of steroid hormones and pharmaceuticals and personal care products with LC–MS/MS in feces of killer whales (Orcinus orca)
Apply the developed method for analysis of those two groups of chemicals

## Slide 7: Material used
Standards and Chemicals
  20 + native chemicals and ~20 isotope labelled compounds
  Solvents (methanol and acetonitrile)
Instrument /Equipment
  Vortexer & Sonication Bath
  Centrifuge & Auto SPE
  LC Column & LC-MS/MS (API 5000)

## Slide 8: Sample preparation
Freeze dry
Wet whale fecal sample
Dried whale fecal sample
Liquid-solid extraction
Centrifugation
Solution
Residue
Dry
Reconstitute
SPE
Dry
Reconstitute
Liquid-liquid extraction
Centrifugation
Upper
Lower
Dry
Reconstitute
Method

## Slide 9: Sample Analysis
Reconstitute
Data & Results
Method
Instrument conditions for target compounds analysis |  |  | 
LC condition | Mobile phase | A: 0.1% (v/v) formic acid in water | B: 0.1% (v/v) formic acid in methanol
 | Total flow | 0.2 mL min−1 | 
 | Column | Xterra MS C18 column (100 mm × 2.1 mm, 3.5 µm) | 
MS condition | Ionization mode | ESI | 
 | IonSpray voltage | + / - 4500 | 
 | Temperature (°C) | 400 | 

## Slide 11
Intraday and interday recoveries and R.S.D. of spiked freeze-dried feces of killer whales |  |  |  |  |  |  |  | 
Compound | Spiked level 1 (5.3 ng /g) |  |  |  | Spiked level 3 (133 ng/g) |  |  | 
 | Intraday |  | Interday |  | Intraday |  | Interday | 
 | RE (%) | RSD (%) | RE (%) | RSD (%) | RE (%) | RSD (%) | RE (%) | RSD (%)
Aldosterone | 116.2 | 0.6 | 104.5 | 7.2 | 84.5 | 1.7 | 89.6 | 5.5
Fluoxetine | 91.2 | 3.8 | 88.1 | 7.9 | 88.7 | 0.8 | 89.3 | 4.3
Cortisone | 120.4 | 8.6 | 122.3 | 4.4 | 130 | 0.7 | 130.3 | 4.2
Cortisol | 99 | 3.3 | 89.3 | 7.6 | 118.2 | 1.9 | 115.6 | 7.9
11-Ketotestosterone | 97.3 | 4 | 95 | 12.1 | 108.8 | 4.8 | 106.9 | 0.8
Corticosterone | 104.1 | 9.6 | 110.8 | 5.4 | 121.5 | 4.8 | 115.6 | 5.7
Estrone | 91.5 | 7.7 | 113.4 | 16.7 | 106.7 | 3 | 102.8 | 3.8
11-Deoxycorticosterone | 124.8 | 3 | 114.5 | 8.5 | 117.8 | 3.3 | 120.1 | 4.7
Testosterone | 102.1 | 2.4 | 107.2 | 2.7 | 96.4 | 1.9 | 96.1 | 1.9
Progesterone | 121.9 | 8.9 | 112.7 | 8.5 | 115.4 | 3.9 | 108.4 | 6.6
Androsterone | 110.6 | 3.7 | 105.9 | 3.5 | 112.7 | 0.7 | 105.2 | 6.6
RE: Recovery; RSD: Relative standard deviation |  |  |  |  |  |  |  | 
Results

## Slide 12
Results
Comparison of available method limit of detection (ng/g) of mammal feces |  |  | 
Compound | Method |  | 
 | Our method | Gesquiere et al | Weltring et al
Cortisone | 0.26 |  | 91.8
Cortisol | 0.65 |  | 18
Corticosterone | 1.52 |  | 99
Androstenedione | 0.37 | 0.25 | 47.4
Testosterone | 0.54 | 0.25 | 54.6
DHEA | 12.76 | 2.5 | 
Progesterone | 1.32 |  | 50.4
Androsterone | 3.7 | 1.5 | 210.6
Estriol | 1.47 |  | 19.2
17b-E2 | 6.36 | 0.25 | 35.4
Estrone | 0.89 | 5 | 88.2

## Slide 13
Chromatograms of hormone and PPCPs in whale feces
Results

## Slide 14: Conclusion
The method for measuring 18 endogenous steroids and 3 pharmaceuticals and personal care products in freeze-dried feces of killer whales has been developed and validated
This method can be used as a reference in the validation of the existed and new immunoassays such as radioimmunoassay and enzyme immunoassay
Hormones such as 17-hydrogenprogesterone, Cortisol, Androstenedione, testosterone, and dehydroepiandrosterone sulfate (DHEAs ) are found and quantified in whale feces
PPCPs such as triclosan, sertraline and fluoxetine are found and quantified in whale feces
A non-invasive approach to characterizing contaminants and health endpoints for killer whales has been developed and validated

## Slide 15: Acknowledgement
SeaWorld
Whales Initiative of Government of Canada